## Slide 1
Simone Spinelli
WP7-T1
GÉANT Automation Platform - GAP
13 December 2023

## Slide 2: WHY ARE WE HERE (TALKING ABOUT AUTOMATION)?
ME:
I am very excited to tell you about our progress
I am looking forward to talk to you after this presentation
YOU:
You want to know more about Automation & Orchestration, or you want to check where we are
You think Automation & Orchestration do not apply to you or maybe you don’t have time for that
You want to know more about the migration of the GÉANT Network
You also want to talk about what we can collectively do about Automation & Orchestration
BOTH:
We are somehow part of GEANT: a community!

## Slide 3: AUTOMATION vs ORCHESTRATION
Needs:
  Change of vendor:
    Copy&paste is not an option
    Lift&shift is not an option (No translation)
    Hybrid period during migration
  Speed/Scale
  Consistency/Predictability
  Service oriented logic
  Converge to something that we can collectively support&maintain
Automation:
Atomic changes: compile a template, do something
Context specific (Nokia/Juniper/Infoblox)
Orchestration:
Represent the business logic
Involves multiple systems
Agnostic to the local context

## Slide 4: MIGRATING TO A NEW VENDOR
New platform is NOKIA 7750SR-S:
  No previous experience with SROS: but it is really close to JunOS – with Caveats
  Relatively small community: but Netconf works as expected
  Brings 400/800G to the edge: a big step towards Terabit network
  Introduces ZR+ optics
Sites organized by TIERS:
  One ring at the time
  Going from the core to the edge and then back
Migration will be in 2 phases:
  PHASE1: Nokia nodes deployed as LSR (starts Q1 2024)
  PHASE2: Nokia nodes promoted to PE (starts Q3 2024)
Totally automated:
  Operators run workflows
  No CLI needed in sunny days

## Slide 5: GAP – MAIN COMPONENTS
Workflow Orchestrator
  Generic, all-purpose orchestrator
  Written in python
  Pydantic as data-model engine
  Takes care of the high-level mechanics
  Developed by SURF and ESNet (and now supported by GÉANT)
Ansible
  Generic automation-engine
  Supported - in some forms - by most of the network brands
  Easy to use, but needs some adjustments
LSO – Lightweight Service Orchestrator
  Gives APIs to call ansible
  Simple, genric, does nothing
  Developed by GÉANT, available on gitlab

## Slide 6: GAP – HIGH LEVEL DESIGN

## Slide 7: GAP – Infrastructure
Deployed with… Ansible 
Everything is shipped as a container:
  Minimal req on hosts
  Dependencies are self-contained
Strict DTAP process:
  Managing Releases is more complicated than we though initially
  Same goes for general packaging and versioning
  Big help from SWD
High availability is more important than performances (for now)

## Slide 8: GÉANT MIGRATION – PHASE 1
Initial deployment
  Boot-config to make the router avaialable via OOB
  Targeted by GAP to deploy base config
Insertion in the network
  First trunk to Juniper: IGP + Multicast feed
  Insertion in tools: router is ready for service
Migration of IPtrunks
  Router starts carrying traffic
  Users and services stay on Juniper

## Slide 9: GÉANT MIGRATION – PHASE 1 – MODELS
* Not all the attributes are shown
Mapping between Products/ProductBlocks and Ansible roles
Special roles for migration
Hierarchy is important to avoid data replication
Hierarchy is important to describe the network
Hierarchy is important. Really

## Slide 10: GÉANT MIGRATION – PHASE 1 – ROUTER_CREATE WORKFLOW

## Slide 11: GÉANT MIGRATION – PHASE 1 – Other workflows
For all subscriptions
  Creation/Modification/Deletion
  Verification workflow still WiP
For Iptrunks
  ISIS metric modification is separated
  Migration is different from modification
For Routers
  Insertion in iBGP mesh
  Insertion in Tools after deployment
Lessons learned:
  Decomposition is very important to keep config objects disjointed
  This is not always possible, so fixes are needed during verification workflows
  A good model facilitates these processes, but we needed few interations to get here
  Mapping Ansible roles to specific workflows/subscriptions also helped

## Slide 12: GÉANT MIGRATION – PHASE 2
Migrating one or more circuit at the time:
  All services insisting on the circuit are migrated together
  All the OSS/BSS systems are updated after migration
  Basic checks are run automatically
Rollback possible until the end of the process
  Config gets deactivated on the source until services are fully migrated
Services on the new platform are functionally equivalent:
  Lots of cleanup
  Customizations will be revised periodically

## Slide 13: GÉANT MIGRATION – PHASE 2 – MODELS & WORKFLOWS
Modeling for phase2 is going to be more complicated (many Products)
  We aim for productBlocks that can be reused
  Correct stitching between physical and logical layer is fundamental: Many services -> One port
Migration workflows should be able to identify the logical dependency and migrate all the services insisting on the port
Verification workflows should be straightforward, but there maybe points of contact between services.
Additional plugins for OSS/BSS will be needed:
  Kentik
  Other internal tooling
A very important chance to rationalize and give more structure to our offer

## Slide 14: GAP – CREDITS & REFERENCES
This work has been done collaborating with many different organizations, so we want to say thanks!
  SURF and ESNet: for the onboarding and all the hints!
  i2CAT/GRNET/CARNET/and others: for all your help in making this (almost) ready
  People in the GOAT team (GÉANT) - You can write us at goat@geant.org:
    Karel
    Aleks
    Mohammad
    Neda
… They are all here, come and talk to us! 
You can find all the code here: https://gitlab.software.geant.org/goat/gap
More info about Workflow Orchestrator: https://workfloworchestrator.org/
More organizations are becoming interested in this, feel free to stop me and ask questions, and stay tuned for TNC24!

## Slide 15
Thank you
Any questions